## Slide 1
📦
SMART SECURE DELIVERY
Smart Secure Delivery
Tracking System
An IoT-based access control and live tracking system for secure last-mile delivery
Device ID: PACKAGE_102

## Slide 2
WHY THIS PROJECT
The Problem With Ordinary Delivery Boxes
🔓
No real access control
Anyone can open a standard delivery compartment — there is no way to verify who is actually the driver.
❓
No visibility in transit
Customers and dispatchers have no live view of where the package is or whether it is still inside.
🚨
Tampering goes unnoticed
A compartment opened early, a missing package, or a diverted route is only discovered after delivery fails.
Our Approach
Combine an NFC access-controlled lock, presence sensing, and live GPS tracking on a Raspberry Pi — all reporting in real time to a dashboard, Telegram, and email, so every stage of the delivery is verified and visible.

## Slide 3
HOW IT FITS TOGETHER
System Architecture
🔧
Physical Layer
▸ NFC reader
▸ IR presence sensor
▸ Servo-controlled lock
▸ GPS (driver phone)
💻
Edge Layer
▸ Raspberry Pi
▸ Local decision logic
▸ Auto-lock timers
▸ Works offline
☁️
Cloud Layer
▸ MQTT broker (HiveMQ)
▸ Real-time pub/sub
▸ Secure TLS link
📱
Application Layer
▸ Node-RED dashboard
▸ Live map
▸ Telegram bot
▸ Email alerts
Data flows left to right on delivery events, and right to left on manual overrides (Unlock / Lock) from the dashboard.

## Slide 4
WHAT'S INSIDE THE BOX
Hardware Components
📶
NFC Reader (PN532)
Identifies the driver card vs. the package tag vs. any unknown card.
🔴
IR Presence Sensor
Confirms the package is physically inside the compartment at all times.
⚙️
Servo-Controlled Lock
Physically opens and locks the compartment door on command.
💡
Status LED
Solid when unlocked, fast-blinking as a visual alarm on security events.
🖥️
Raspberry Pi
Runs the control logic and publishes every event over MQTT.
📍
GPS (OwnTracks)
Streams live driver location for geofencing and route tracking.
All Connected Through One Raspberry Pi
The Pi reads the NFC reader and IR sensor, drives the servo and LED directly over GPIO, and publishes every state change to the cloud over MQTT — so the physical hardware and the software dashboard always agree.

## Slide 5
THE HAPPY PATH
Normal Delivery Flow
🪪
1
Driver Scans Card
Authorized NFC card is recognized
🔓
2
Door Opens
Servo unlocks; a 10s loading timer starts
📦
3
Package Loaded
Package tag detected inside the window
🔒
4
Auto-Lock
After 5s the compartment locks itself
🚚
5
In Transit
GPS + IR monitor the shipment live
🏁
6
Arrived
Geofence confirms arrival at destination
Every step above publishes a status update over MQTT — the dashboard, Telegram, and map update within a second of the physical event.

## Slide 6
THE COMPLETE PICTURE
Full System Flow — All Scenarios
Process
Decision
Success
Alert
Unauthorized Alert
(Telegram)
≥ 3
Attempts?
Yes
Critical Email
Alert
No
Resume Monitoring
NFC Card
Scanned
Authorized
UID?
No
Yes
Driver or
Package?
Pkg only
Logged Only —
Door Stays Closed
Driver
Door Opens —
10s Loading Timer
Loaded
in Time?
Yes
5s Timer → Auto-Lock
→ In Transit
No (10s up)
Auto-Lock — Security
Alert + Email Sent
Package
Absent >10s?
Yes
Package Missing —
Alert + Email
IR sensor, checked only while IN_TRANSIT
Outside Geofence
Radius?
Yes
Route Deviation —
Alert + Email
No
Arrived ✅

## Slide 7
WHEN SOMETHING'S WRONG
Security & Exception Scenarios
🚫
Unknown Card
Any UID that isn’t the driver’s or the package’s triggers an instant Telegram alert. The LED blinks as a physical alarm; the 3rd repeat attempt escalates to a critical email.
⏱️
Opened Without Loading
If the driver opens the door but no package is scanned within 10 seconds, the system auto-locks itself and immediately emails a critical alert — no waiting for a repeat.
📤
Package Missing in Transit
The IR sensor watches for the package only while the shipment is IN_TRANSIT. If it’s absent for more than 10 seconds, a missing-package alert and email fire right away.
🧭
Route Deviation
Live GPS is checked against the destination geofence. A serious deviation from the expected route sends a one-time alert and email so dispatch can intervene.

## Slide 8
WHERE IS IT RIGHT NOW?
Live Tracking & Geofencing
🗺️ Live Worldmap (Node-RED)
🚚
Vehicle
🏁
Destination
geofence radius
Location Source
The driver’s phone streams GPS via OwnTracks to the same MQTT broker.
Geofence Check
Every location update is compared against the destination coordinates and a set radius.
Arrival Detection
Once the vehicle enters the radius while IN_TRANSIT, status flips to ARRIVED and the team is notified.
Deviation Alert
Straying far off the expected route triggers a one-time route-deviation alert and email.

## Slide 9
STAYING IN THE LOOP
Dashboard, Telegram Bot & Alerts
📱 Node-RED Dashboard
📦 PACKAGE_102
IN_TRANSIT
🔒 Lock
LOCKED
📦 Present
YES
📍 Location
31.22, 30.51
🚨 Attempts
0
🔓 Unlock
🔒 Lock
Manual override buttons let a dispatcher unlock or lock remotely at any time.
✈️
Telegram Bot
Every event — driver access, package loaded, locked, alerts — is pushed instantly as a message. Dispatchers can also query the bot directly:
/status → full delivery state
/location → current GPS
📧
Critical Email Alerts
Reserved for events that need immediate human attention — escalated beyond a chat message:
Opened without loading
Package missing in transit
Repeated unauthorized access (3+)
Serious route deviation

## Slide 10
KEY TAKEAWAYS
A Delivery You Can Actually Trust
🔐
Verified Access
Only the recognized driver card can open the compartment — every other attempt is logged and alerted.
👁️
Full Visibility
Live status, location, and history are always one glance (or one message) away.
⚡
Real-Time Response
Security events reach the team in under a second, with critical cases escalated to email.
🧩
Modular & Extensible
Built on MQTT and Node-RED, so new sensors, routes, or alert channels drop in easily.
Thank you — questions welcome.